## Slide 1
1
Enhance Performance
Computation Methods of C.Elegans
Mohd Sadique
Under the guidance of :
Professor Ioan Raicu
Notes: 1

## Slide 2
Flow of the presentation
Brief Overview
MOTIVATION
DESIGN AND IMPLEMENTATION
EVALUATION
RESULTS
PROFILING
Conclusion
Future Work

## Slide 3
Brief Overview
C.Elegans are a type of roundworm
C. Elegans locomotory behavior can be recorded and analyzed with computational and mathematical tools.
Our tracking system was designed to accommodate worms that explore a large area with frequent turns and reversals at high speeds.
worm traking system which consisting of both hardware and software
Tracking software is responsible for capturing the image of the worm movement in the agar plate
Worm Segmentation is an image processing application developed in C++.
Centroid prediction during blurring and threshold calculation

## Slide 4
READ JPEG IMAGE
Decode Image into 24 bit per pixel
Convert into 8bit Grey Scale Image
Convert in Blur Image
Binary Image By Threshold
Find Largest Component
Code Flow

## Slide 5
Motivation & Challenges
Reduce largest component processing time. Initially it takes 95% processing Time.
Enhance the performance and to reduce processing time to process single frames per seconds.
Support higher Resolution of frames
Process frames more than 100fps of higher resolution 4k.
Reduce or Remove noise in the C. elegans frames.

## Slide 6
DESIGN AND IMPLEMENTATION
Enhancement : Segmenter Algorithm
Design-1 Sequential image Implementation(P1)
Design-2 Parallel frame Implementation(P2)
Design-3 Buffer Pool Implementation (P3)

## Slide 7
Enhancement : Segmenter Algorithm
Initially the application has 4 different components
JPEG read & decoder 2.Image blurring algorithm 3.Threshold algorithm
4. Largest component calculation
Then Merge two component to enhance performance
JPEG read & decoder 2.Image blurring_threshold algorithm
3. Largest component calculation
Modified Blur_Threshold Aglorithm to increase computation efficiency.
Implemented Register variable which work more than 100 times faster then normal variable.
Most high performance CPUs will have ~100 physical registers

## Slide 8
READ JPEG IMAGE
Decode Convert into 8bit Grey Scale Image
Convert in Blur Image &
Binary Image By Threshold
(Predict Temp Centroid)
Find Largest Component
NEW Code Flow
High Density pixel position
Use Register Variables

## Slide 9
Blur_Threshold Aglorithm
Input: image(pixel array, width, height)
Output: BlurImage, TCx,TCy (temperory Centroid)
TCx=0,TCy=0 ,Tarea=0
for each pixel i in the image; do
for each neighbor i of pixel; do
sum = (add all neighbor pixel value)/ neighbor
endfor
if(sum >threshold value )
BlurImage = sum/(No. of Neighbours);
Tcx=x ;Tcy=y;Tarea++;
Else
blurImage =0
end if
endfor
TCx = TCx/area ; TCy = TCy/area;

## Slide 10
LARGEST COMPONENT ALGORITMS
Input: image(pixel array, width, height,TCx,TCy)
Output: LargestCount(Count of largest connected component)
largestComponent_pixel_count = 0
for each pixel from TCx ,TCy ±25 pixel.
if i is true;
LargeCount= find_connected_components(i, image)
endif
If LargeCount > 80% of AvgArea then
Return LargeCount
endif
Endfor
for each pixel i in the image; do
if i is true; then
count=0;
LargeCount = find_connected_components(i, image, &count)
if LargeCount > largest_component_pixel_count ; then
largest_component_pixel_count = LargeCount
endif
endif
endfor

## Slide 11
FIND CONNECTED COMPONENTS
Input: pixel(x, y cordinates of pixel) image(pixel array, width, height) *count
Output: count of pixels in this connected component
set i to false ;
for each neighbor i of pixel; do
if i is true; then
*count += find_connected_components(i, image)
endif
Endfor

## Slide 12
Design-1 Sequential frame Implementation(P1)
In this implementation all images sequentially divided among different threads eg. Thread1 have 0 – 99 images and thread2 have 100 to 199.
Each thread first read image then decode and convert into gray scale image of 8bit data per pixel.
If its 1st image then entire image is processed and convert into blurred image and calculated centroid and area of elegans.
If any thread process 2nd image then it takes small window of image based on previous image centroid and then process window of image
Image1
Image99
……
Thread1
Image100
Image199
……
Thread2
………………….

## Slide 13
Design-2 Parallel frame Implementation(P2)
In this implementation all images distributed among different threads based on first come first service bases. eg. Thread1 have 1st images and thread3 have 2nd image
Each thread first read image then decode and convert into gray scale image
of 8bit data per pixel.
Centroid is shared among different Pthread by global variables. Sequence of all threads is maintained by Mutex lock in Pthread
    pthread_mutex_lock(&lock);
    if(GlobalPointer>=Total_Images) break;
    int assign= GlobalPointer ++;
    pthread_mutex_unlock(&lock);
Image1
Image2
Thread1
Thread2
Image3
Thread3
…………
…………

## Slide 14
Design-3 Buffer Pool Implementation (P3):
All Pthread is divided among two section.
In First Section, No. of Pthread perform read, decode and Convert into 8 Bit GrayScale image.
In Second Section No. of Pthread perform computation on image like implementing blurring and threshold algorithm and finding largest component.
Buffer Pool is created by producer- consumer algorithm.
Three different mutex lock is used to synchronized all process.
Image1
Image2
Thread1
Thread2
Compute Image1
Thread3
…
Buffer Pool
…
Compute Image2
Thread4
…
…

## Slide 15
Second Mutex Lock: To store decoded image into buffer pool
pthread_mutex_lock(&lock2);
Gbuffer[gs]=buffer;
GPos[gs]=i;
pthread_mutex_unlock(&lock2);
Third Mutex Lock: To Read Decoded image form buffer pool
pthread_mutex_lock(&lock3);
if(gf<gs)
fs=gf++;
pthread_mutex_unlock(&lock3);
Read(Gbuffer[fs];
Three different mutex lock is used to synchronized all process.
First Mutex Lock: Read filename position for the list.
pthread_mutex_lock(&lock);
if(GlobalPointer>=Total_Images) break;
      int assign= GlobalPointer ++;
      pthread_mutex_unlock(&lock);

## Slide 16
EVALUATION
All pthread tasks are tested in a Chameleon cloud bare metal system. The system
is configured with 24 cores and 128GB memory.
The test data consisted of 47000 images of varying resolutions – 640x480, 720x480,
1280x720, 1920x1080, 3840x2160.
New dataset which of 187000 images of 1280X720 resolutions and 250000 images
of resolution of 640X480

## Slide 17
RESULTS
    Weak Scalling Test on resolution 1280x960
No. Of Threads | Total Frames | Execution Time (P1) | Execution Time (P2)
1 | 1000 | 19.2278 | 19.0932
2 | 2000 | 19.4201 | 19.39
4 | 4000 | 19.706 | 19.78
8 | 8000 | 21.7095 | 21.8043
12 | 12000 | 23.2313 | 24.4524
24 | 24000 | 23.6888 | 24.8651
48 | 48000 | 43.0521 | 44.5467
96 | 96000 | 81.0976 | 83.245
192 | 192000 | 218.666 | 172.45
Chart: Week scaling Performance
| 1 | 2 | 4 | 8 | 12 | 24 | 48 | 96 | 192
Execution Time (P1) | 19.2278 | 19.4201 | 19.706 | 21.7095 | 23.2313 | 23.6888 | 43.0521 | 81.0976 | 165.011
Execution Time(P2) | 19.0932 | 19.39 | 19.78 | 21.8043 | 24.4524 | 24.8651 | 44.5467 | 83.245 | 172.45

## Slide 18
    No. of Frames Computed on Resolution 1280x960
No. Of Threads | Total Frames | Frames/ Sec(P1) | Frames/ Sec(P2)
1 | 1000 | 52.01 | 52.37
2 | 2000 | 102.99 | 103.15
4 | 4000 | 202.98 | 202.22
8 | 8000 | 368.5 | 366.9
12 | 12000 | 516.54 | 490.75
24 | 24000 | 1013.14 | 965.21
48 | 48000 | 1114.93 | 1077.52
96 | 96000 | 1183.76 | 1153.22
192 | 192000 | 1163.56 | 1113.37
Chart: Frames per sec
| 1 | 2 | 4 | 8 | 12 | 24 | 48 | 96 | 192
Frames/Sec(P1) | 52.008 | 102.9861 | 202.9839 | 368.5023 | 516.5445 | 1013.137 | 1114.9282 | 1183.7588 | 1163.5588
Frames/Sec(P2) | 52.3747 | 103.146 | 202.2245 | 366.9001 | 490.7494 | 965.2083 | 1077.5209 | 1153.2224 | 1113.3662

## Slide 19
    Weak Scalling Test on resolution 640x480
No. Of Threads | Total Frames | Execution Time (P1) | Execution Time(P2)
1 | 1000 | 5.94828 | 5.8475
2 | 2000 | 6.02886 | 6.0241
4 | 4000 | 6.13948 | 6.2145
8 | 8000 | 6.13948 | 6.4512
12 | 12000 | 7.53171 | 7.5642
24 | 24000 | 8.5178 | 8.6457
48 | 48000 | 15.3293 | 15.4235
96 | 96000 | 31.566 | 32.6578
192 | 192000 | 60.878 | 62.3657
Chart: Week Scaling performance
| 1 | 2 | 4 | 8 | 12 | 24 | 48 | 96 | 192
Execution Time (P1) | 5.9483 | 6.0289 | 6.1395 | 6.1395 | 7.5317 | 8.5178 | 15.3293 | 31.566 | 60.878
Execution Time(P2) | 5.8475 | 6.0241 | 6.2145 | 6.4512 | 7.5642 | 8.6457 | 15.4235 | 32.6578 | 62.3657

## Slide 20
    No. of Frames Computed on Resolution 640x480
No. Of Threads | Total Frames | Frames/ Sec(P1) | Frames/ Sec(P2)
1 | 1000 | 168.12 | 171.01
2 | 2000 | 331.74 | 332
4 | 4000 | 651.52 | 643.66
8 | 8000 | 1303.04 | 1240.08
12 | 12000 | 1593.26 | 1586.42
24 | 24000 | 2817.63 | 2775.95
48 | 48000 | 3131.26 | 3112.13
96 | 96000 | 3041.25 | 2939.57
192 | 192000 | 3153.85 | 3078.62
Chart: Frames per Sec
| 1 | 2 | 4 | 8 | 12 | 24 | 48 | 96 | 192
Frames/Sec(P1) | 168.1158 | 331.7377 | 651.521 | 1303.042 | 1593.2637 | 2817.629 | 3131.2584 | 3041.2469 | 3153.8487
Frames/Sec(P2) | 171.0133 | 331.9998 | 643.656 | 1240.0794 | 1586.4202 | 2775.9464 | 3112.1341 | 2939.5734 | 3078.6153

## Slide 21
No. Of Threads | Read Threads | Process Threads | Execution Time | Frames /Sec
24 | 19 | 5 | 27.6958 | 866.56
24 | 20 | 4 | 26.106 | 919.33
24 | 21 | 3 | 24.1937 | 991.99
24 | 22 | 2 | 22.5431 | 1064.63
24 | 23 | 1 | 44.0708 | 544.58
Chart: Execution Time (24000 Frames on 24 threads)
| 19 | 20 | 21 | 22 | 23
Execution Time (1000 Frames / threads) | 27.6958 | 26.106 | 24.1937 | 22.5431 | 44.0708
Buffer pool implementation for Resolution 1280x960 on 24 threads

## Slide 22
Buffer pool implementation for Resolution 1280x960 on 48 threads
No. Of Threads | Read Threads | Process Threads | Execution Time | Frames /Sec
48 | 40 | 8 | 42.2249 | 1136.77
48 | 41 | 7 | 41.1732 | 1165.81
48 | 42 | 6 | 40.8691 | 1174.48
48 | 43 | 5 | 39.8936 | 1203.2
48 | 44 | 4 | 43.6869 | 1098.73
48 | 45 | 3 | 53.1683 | 902.79
Chart: Execution Time (48000 Frames on 48 Thread
| 40 | 41 | 42 | 43 | 44 | 45 | 46
Execution Time | 42.2249 | 41.1732 | 40.8691 | 39.8936 | 43.6869 | 53.1683 | 66.0989

## Slide 23
Buffer pool implementation for Resolution 640x480 on 24 threads
No. Of Threads | Read Threads | Process Threads | Execution Time | Frames/Sec
24 | 17 | 7 | 9.231 | 2599.94
24 | 18 | 6 | 8.7435 | 2744.90
24 | 19 | 5 | 8.4578 | 2837.62
24 | 20 | 4 | 8.6123 | 2786.71
24 | 21 | 3 | 11.1937 | 2144.06
24 | 22 | 2 | 13.4572 | 1783.43
24 | 23 | 1 | 17.1423 | 1400.05
Chart: Execution Time (24000 Frames on 24 threads)
| 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 9.231 | 8.7435 | 8.4578 | 8.6123 | 11.1937 | 13.4572 | 17.1423

## Slide 24
Buffer pool implementation for Resolution 640x480 on 24 threads
No. Of Threads | Read Threads | Process Threads | Execution Time | Frames/Sec
24 | 17 | 7 | 9.231 | 2599.94
24 | 18 | 6 | 8.7435 | 2744.90
24 | 19 | 5 | 8.4578 | 2837.62
24 | 20 | 4 | 8.6123 | 2786.71
24 | 21 | 3 | 11.1937 | 2144.06
24 | 22 | 2 | 13.4572 | 1783.43
24 | 23 | 1 | 17.1423 | 1400.05
Chart: Execution Time (24000 Frames on 24 threads)
| 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 9.231 | 8.7435 | 8.4578 | 8.6123 | 11.1937 | 13.4572 | 17.1423

## Slide 25
Buffer pool implementation for Resolution 640x480 on 48 threads
No. Of Threads | Read Threads | Process Threads | Execution Time | Frames /Sec
48 | 32 | 16 | 17.9352 | 2676.30
48 | 34 | 14 | 15.8342 | 3031.41
48 | 36 | 12 | 15.1543 | 3167.42
48 | 38 | 10 | 15.6452 | 3068.03
48 | 40 | 8 | 17.6743 | 2715.81
48 | 42 | 6 | 20.5363 | 2337.32
48 | 44 | 4 | 29.2454 | 1641.28
Chart: Execution Time (48000 Frames on 48 threads)
| 32 | 34 | 36 | 38 | 40 | 42 | 44
Execution Time | 17.9352 | 15.8342 | 15.1543 | 15.6452 | 17.6743 | 20.5363 | 29.2454

## Slide 26
Multi Core Test results
Java and C++ result compared with new dataset of resolution 640*480 and 1280x960
Old dataset with of resolution 720x480, 1280x720, 1920x1080 and 3840x2160.
Resolution | Java | C++
640x480 | 89.748 | 7.927
720x480 | 145.124 | 9.360
1280x720 | 345.505 | 19.235
1280x960 | 475.345 | 24.235
1920x1080 | 876.247 | 45.125
3840x2160 | 3034.611 | 163.384
Chart: Computation between Java & C++
| 640x480 | 720x480 | 1280x720 | 1280x960 | 1920x1080 | 3840x2160
Java | 89.7485 | 145.1236 | 345.5052 | 475.345 | 876.2466 | 3034.6105
C++ | 7.9265 | 9.3597 | 19.2345 | 24.2345 | 45.1246 | 163.3844

## Slide 27
PROFILING
Java and C++ implementation were profiled to see the performance of individual component
JPEG read & Decorder, Blur_threshold algorithm and largest component algorithm.
  Loading Image
640x480 | 13.462 | 7.292
720x480 | 21.769 | 8.611
1280x720 | 51.826 | 17.696
1280x960 | 71.302 | 22.296
1920x1080 | 131.437 | 41.515
3840x2160 | 455.192 | 150.314
Chart: Read Image, Decode and convert into Gray Scale
| 640x480 | 720x480 | 1280x720 | 1280x960 | 1920x1080 | 3840x2160
Java | 13.4623 | 21.7685 | 51.8258 | 71.3017 | 131.437 | 455.1916
C++ | 6.7375 | 7.9557 | 16.3493 | 20.5993 | 38.3559 | 138.8767

## Slide 28
Image Blur and Thresholding Computation
Resolution | Java | C++
640x480 | 44.874 | 1.823
720x480 | 72.562 | 0.842
1280x720 | 172.753 | 1.731
1280x960 | 237.673 | 2.181
1920x1080 | 438.123 | 4.061
3840x2160 | 1517.305 | 14.705
Chart: Image Blur & Threshold computation
| 640x480 | 720x480 | 1280x720 | 1280x960 | 1920x1080 | 3840x2160
Java | 44.8742 | 72.5618 | 172.7526 | 237.6725 | 438.1233 | 1517.3053
C++ | 1.8231 | 0.84237 | 1.7311 | 2.1811 | 4.0612 | 14.7046

## Slide 29
  Largest Component
Resolution | Java | C++
640x480 | 31.412 | 0.476
720x480 | 50.793 | 0.562
1280x720 | 120.927 | 1.154
1280x960 | 166.371 | 1.454
1920x1080 | 306.686 | 2.707
3840x2160 | 1062.114 | 9.803
Chart: Largest ComponentComputation
| 640x480 | 720x480 | 1280x720 | 1280x960 | 1920x1080 | 3840x2160
Java | 31.412 | 50.7932 | 120.9268 | 166.3707 | 306.6863 | 1062.1137
C++ | 0.47559 | 0.56158 | 1.1541 | 1.4541 | 2.7075 | 9.8031
. Java drastically slower as compare to C++ code. In C++ temporary centroid is predicted based on high pixel density and first calculate at that location
if area is larger then 80% of AvgArea of C.elegans then return area with centroid. Else it check entire image for largest area.

## Slide 30
Conclusion:-
C++ performance during Bluring , threshold and Largest component is improved drastically it atleast 100 time faster then java code due to largest component prediction method during bluring and threshold calculation.
Buffer Pool implementation works better then other implementation in some scernios
Implementation of the segmentation. C++ implementation is bottleneck is Reading JPEG image file during this process image is decoded converted into 24bit pixel and then again converted into 8Bit gray scale image. Which takes 90% of overall performance.

## Slide 31
Future Work
According to C++ Implementation the bottleneck is read jpeg image and convert into grayscale image. To improve image processing performance gpu_image_processing should be implemented to decode jpeg image into gray scale image with higher performance.
Needs to work on new algorithm which effectively trace multiple elegans at same with higher resolutions and faster frames processing.

## Slide 32: THANK YOU

## Slide 33
References
Moy K, Li W, Tran HP, Simonis V, Story E, Brandon C, et al. (2015). “Computational Methods for Tracking, Quantitative Assessment, and Visualization of C.elegans Locomotory Behavior” PLoS ONE 10 (12): e0145870. doi/10.1371/journal.pone.0145870
Aditya Shirodkar, Chiranjeevi Ankamreddy, Calin Segarceanu Ioan Raicu. Benchmarking Worm Segmenter
Sjie Jason Wang, Zhao-Wen Wang (2013). “Track-A-Worm, An OpenSource System for Quantitative Assessment of C.elegans Locomotory and Bending Behavior”. PLoS ONE 8(7): e69653. doi:10.1371/journal.pone.0069653
Derek Bradley, Gerhard Roth. Adaptive Thresholding Using Integral image.
Leifer AM, Fang-Yen C, Gershow M, Alkema MJ, Samuel AD. Optogenetic manipulation of neural activity in freely moving Caenorhabditis elegans. Nat Methods. 2011; 8(2):147–52. doi: 10.1038/nmeth.1554
Enhance Performance of computation methods of C.Elegans. Piyush Nath, Ioan Raicu, Daniela Raicu
Steven J Husson, Wagner Steuer Costa, Cornelia Schmitt, Alexander Gottschalk et al. (2012). “Keeping
Ramot D, Johnson BE, Berry J T L, Carnell L,
Adelina Voukadinova, Tejus Prasad, Ioan Raicu, Daniela Raicu (2016) “Improving the Performance of C.Elegans RoundWorm Tracking and Segmentation.
Goodman MB. The Parallel Worm Tracker: a platform for measuring average speed and drug-induced paralysis in nematodes. PLoS One. 2008; 3(5):e2208. doi: 10.1371/journal.pone.0002208